## Slide 1: Great Energy Predictor for Buildings
Kaggle competition by ASHRAE

## Slide 2: Agenda
01
Kaggle competition Great Energy Predictor
02
Machine Learning Deployment
03
Further Improvements
04
Machine Learning Applications in the Built Industry

## Slide 3: Machine Learning Applications in the Built Industry
Digital Technologies
Energy Engineering
Objectives
Save up to 25% in energy bills and reduce your carbon footprint
Real-time analytics / FDD and ML models insights with BMS data
Minimize Critical Equipment Downtime
The Global Goals for Sustainable Development

## Slide 4: Machine Learning Applications in the Built Industry
A
Identify Anomoaly
Abnormal Readings from IoT sensors / Power surging etc
C
Optimize Energy Usage
Deviations can be analyzed in real time for insights and remedial measures
D
Predictive Mainteance
Improve predictive maintenance scheduling
B
Optimize Setpoint
Optimize controls based on real-time/ envionmental factors

## Slide 5: ASHRAE Great Energy Predictor III
The American Sociery of Heating, Refrigerating and Air-Conditioning Engineers
The Great Energy Predictor III from ASHRAE aims to develop counterfactual models to predict building energy usage based on historic data and observed weather.
Goal to improve estimations of these energy-saving initiatives, allowing large-scale investors and financial institutions to be more willing to invest in building efficiencies.

## Slide 6: Competition Goal: To build a regression model that predicts metered building energy usage meter
Water-Cooled Chiller System
Absorption Chiller
Chilled Water
Washing
Showering
Drinking
Hot Water
HVAC
Lightings
Ventilation
Plug Loads
Electricity
Sterilization for medical and food processing facilities
Steam

## Slide 7: Datasets
The dataset includes three years of hourly meter readings from over
one thousand buildings at several different sites around the world.
Train dataset (2016)
20 millions historical usage data from around 1600 buildings,
16 different sites and 4 different meters
Test Dataset (2017-2018)
42 millions historical usage data from same buildings
but different period of time
Weather Data
Building Metainfo
Meters historical usage
Merged Data (3 years timeframe)
Train
Test
Notes: In the case of RMSE, the presence of outliers can explode the error term to a very high value. But, in the case of RMLSE the outliers are drastically scaled down therefore nullifying their effect.
In simple words, more penalty is incurred when the predicted Value is less than the Actual Value. On the other hand, Less penalty is incurred when the predicted value is more than the actual value. This is especially useful for business cases where the underestimation of the target variable is not acceptable but overestimation can be tolerated.

## Slide 8: Dataset Preprocessing: Identifying outlier building
Notes: Building 1099 is a clear anomaly (refer to plot below). Given its GFA, the building is unlikely to consume so much energy. It's possible that the meters aren't working properly or that the meter readings are cumulative.

## Slide 9: Dataset Preprocessing: Removing Building with anomaly consumption
Notes: Building 1099 is a clear anomaly (refer to plot below). Given its GFA, the building is unlikely to consume so much energy. It's possible that the meters aren't working properly or that the meter readings are cumulative.

## Slide 10: Dataset Preprocessing
Smoothed temperature data
    Rolling averages are useful for finding long-term trends otherwise disguised by occasional fluctuations
Missing Data
    Filling in missing temperature data with linear interpolation is a simple but effective approach to improve model performance
Anomaly removal
    With some domain expertise in meters and simple intuition, abnormal readings for the four meters were detected and dropped
Feature Engineering
    Add in feels like temperature, wind chill, and heat index
Notes: With some domain expertise in meters and simple intuition, abnormal readings for the four meters were detected and dropped
Remove long streaks of constant 0 readings from electric meters
Identifying abnormal hot water/steam and chilled meter consumption in each facility during the winter and summer seasons
A transformation of the target variable that brings it closer to a normal distribution

## Slide 11: Dataset Preprocessing
Before Logarithm Transformation
After Logarithm Transformation
Notes: With some domain expertise in meters and simple intuition, abnormal readings for the four meters were detected and dropped
Remove long streaks of constant 0 readings from electric meters
Identifying abnormal hot water/steam and chilled meter consumption in each facility during the winter and summer seasons
A transformation of the target variable that brings it closer to a normal distribution

## Slide 12: Exploratory Data Analysis
Education, service facilities consume most energy
Meter 2: steam consume most energy, followed by Meter 1: chilledwater
Notes: Building 1099 is a clear anomaly (refer to plot below). Given its GFA, the building is unlikely to consume so much energy. It's possible that the meters aren't working properly or that the meter readings are cumulative.

## Slide 13: Exploratory Data Analysis
Increased usage throughout the summer (June-Sept) and winter (December-March) seasons
Notes: Building 1099 is a clear anomaly (refer to plot below). Given its GFA, the building is unlikely to consume so much energy. It's possible that the meters aren't working properly or that the meter readings are cumulative.

## Slide 14: Feature Selection
Using Leave One Feature Out Analysis
The top features are square feet, building id, primary use, and building counts per site.
Notes: Building 1099 is a clear anomaly (refer to plot below). Given its GFA, the building is unlikely to consume so much energy. It's possible that the meters aren't working properly or that the meter readings are cumulative.

## Slide 15: Training Pipeline
Training Dataset
Preprocessing
Train Set without Leak
GRUs
XGB
Group Kfolds by Building
Weighted-average Ensembling
Final Model Submission (Kaggle score 1.197 RMSLE)
Notes: Building 1099 is a clear anomaly (refer to plot below). Given its GFA, the building is unlikely to consume so much energy. It's possible that the meters aren't working properly or that the meter readings are cumulative.

## Slide 16: Competition metric: Root Mean Squared Logarithmic Errror
Unique Properties:
Robustness to the effect of the outliers
RMSLE incurs a larger penalty for the underestimation of the Actual variable than the Overestimation.
Notes: In the case of RMSE, the presence of outliers can explode the error term to a very high value. But, in the case of RMLSE the outliers are drastically scaled down therefore nullifying their effect.
In simple words, more penalty is incurred when the predicted Value is less than the Actual Value. On the other hand, Less penalty is incurred when the predicted value is more than the actual value. This is especially useful for business cases where the underestimation of the target variable is not acceptable but overestimation can be tolerated.

## Slide 17: Use Case 1: Chiller Plant Predictive Analytics Mixed-building Singapore
Independent Variables Selected:
Chilled Water Flow
Chilled Water Return-Supply Temp
Condenser Water Flow
Condenser Water Supply-Return Temp
Dataset Summary:
Dataset timeline: 01/01/2019 – 15/03/2019
Training period: 2.5 months
Logging interval: every 1 minute
Weather Normalization: No
Target Variable: Dependent Variable
Chiller Power Consumption

## Slide 18: Use Case 1: Chiller Plant Predictive Analytics Mixed-building Singapore (Infographics)

## Slide 19: Use Case 1: Chiller Plant Predictive Analytics Mixed-building Singapore (Infographics)

## Slide 20: Use Case 2: Solar Thermal & Absorption Chiller Predictive Analysis (Solar Thermal System Energy Flow Diagram)

## Slide 21: Use Case 2: Solar Thermal & Absorption Chiller Predictive Analysis (Model KPI - Predicting F2 Normalized Thermal Output)

## Slide 22: Use Case 2: Solar Thermal & Absorption Chiller Predictive Analysis (Infographics)

## Slide 23: Further Improvements
01 | Remove consumption spikes that are difficult to forecast, making the prediction more volatile
02 | Use first and second differentiation of temperature data to make non-stationary data stationary and add rate of change information to the model
03 | One hot encode building_id and site_id before modeling (computationally expensive)
04 | Experiment with lagged weather features and how it affects the model's success metrics
05 | Experiment relations of existing features and target variable (prediciting kwh/ft2 instead)

## Slide 24
To Divya , Samantha Shao Quan, Ben
Thanks for making learning fun!